OpenWRT Recovery
# YOU HAVE TO OPEN THE ROUTER….
- Connect serial cable PC→router
- Connect Ethernet Cable LAN1 (any just remember) to PC
- Force static address at PC end of 192.168.1.2
- Open Putty as root (screen is awful and will not show all characters)
  - Find serial device (/dev/ttyUSB0 or similar, use sudo dmesg -w and unplug/replug it to see)
    - Set Baud to 115200
    - Set Control Flow in Connection→Serial to NONE
    - Click Open
- Plug in Router Power, and stuff should appear
- At about 11.xxxx the ‘press F and then return’ should pop up, quickly do that
- Shell should appear, clearly stating you are in failsafe mode, if not and just a normal shell, powercycle router and retry
- Make sure we can write files by executing mount_root
- Use ip addr to see if we have a connection (should be 192.168.1.1)
  - If we do, try and ssh root@192.168.1.1 from PC
    - If that doesn’t work or the connection is configured badly or not at all:
      - delete all configured ip addresses
      - ip addr del <ip address>/<netmask> dev <device name, eg eth0>
      - make sure ONLY the lan<number>@eth0 connection you are plugged into has an ip
      - ip addr add 192.168.1.1/24 dev lan<number> NO @eth0
      - ip link set lan<number> up AGAIN NO @eth0
        - If it still doesn’t work maybe:
          - ip route add default via 192.168.1.1 dev lan<number> AGAIN NO @eth0
- In a new terminal window on your PC, download/build/whatever a hopefully working firmware and then:
  - scp <sysupgrade firmware path and filename> root@192.168.1.1:/
    - If it complains, which it will, delete the offending line in ~/.ssh/known_hosts and retry
- Back in Putty, once the scp has finished, issue the command:
  - sysupgrade -n -F /<name of firmware>
- Cross your fingers, and once finished (monitor in Putty), plug the Ethernet cable back into the network and see if it work…
  - If not, just keep on redoing this with different firmwares until it does
- Remove static IP from PC interface
DONE!!!

# Other Possible Solutions:
- Hopefully usb should be working
- Transfer over serial using lrz -Z on the router and sz --zmodem [PATH TO FIRMWARE] > /dev/ttyUSB0 < /dev/ttyUSB0 on the PC, then sha256sum on router and PC to make sure it went across okay